|  | EUROPEAN COMMISSION DIRECTORATE-GENERAL FOR ENERGY Directorate C - Renewables, Research and Innovation, Energy Efficiency C.3 - Energy efficiency |
| --- | --- |

Brussels, 4 April 2014

Working Document

on the Omnibus Review Process of existing measures

- Agenda Point 7 –

This Working Document will be discussed with the Members of the Ecodesign Consultation Forum at the meeting of 5 May 2014 (agenda point 7).

I. Introduction

The purpose of this Working Document is to present the results of the study on the Omnibus Review Process of the existing measures (domestic refrigeration products, washing machines, dishwashers, washer dryers, simple set-top boxes and water pumps) and to suggest the way forward.

II. General context

Twelve existing regulations are being reviewed in the light of technological progress in 2012 -2014, as required in the regulations themselves. This concerns regulations on:

- external power supplies – Commission Regulation (EC) No 278/2009 (Ecodesign);

- televisions - Commission Regulation (EC) No 642/2009 (Ecodesign) - Commission Regulation (EU) No 1062/2010 (Labelling);

- lighting products

  - non-directional household lamps - Commission Regulation (EC) No 244/2009 (Ecodesign);

  - fluorescent lamps without integrated ballast for high intensity discharge lamps and for ballasts and luminaires - Commission Regulation (EC) No 245/2009 (Ecodesign);

- household dishwashers - Commission Regulation (EU) No 1016/2010 (Ecodesign) - Commission Regulation (EU) No 1059/2010 (Labelling);

- household washing machines - Commission Regulation (EU) No 1015/2010 (Ecodesign) - Commission Regulation (EU) No 1061/2010 (Labelling);

- household refrigerating appliances - Commission Regulation (EC) No 643/2009 (Ecodesign) - Commission Regulation (EU) No 1060/2010 (Labelling);

- simple set top boxes - Commission Regulation (EC) No 107/2009 (Ecodesign).

The reviews of the regulations on external power supplies and televisions follow individual paths. The review of external power supplies foresees an up-date of the requirements and a minor adaptation of the scope. The review of the televisions was combined with the development of a measure on displays, due to fast technology development and similarities in usage and technologies. Inter-service consultations for these two product groups are foreseen later this year.

As regards the review of the so-called 'stage 6' requirements of Regulation 244/2009 on non-directional household lamps, which relates to halogen lamps, a consultation forum meeting took take place in November 2013 and the measure is being taken forward.

III. Omnibus review report

a) Introduction

The rest of these existing regulations (i.e. 9 regulations on lighting products, dishwashers, washing machines, refrigerating appliances and simple set top boxes) have been covered by an omnibus-like review study. In addition to these regulations, the study also included the existing 'washer dryers' Commission Directive 96/60/EC and the review of the tolerances in Commission Regulation (EU) No 547/2012 on water pumps. The review study started in June 2013 and concluded in March 2014 after a stakeholder meeting in November 2013.

b) Objectives of the report

The objective of this exploratory study was to identify whether there are sufficient potential savings to justify changing the regulations. This approach was agreed with stakeholders at the horizontal Consultation Forum meeting in April 2012. The analysis focused on possible energy savings as basis for prioritisation, but also considers resource efficiency aspects insofar as feasible within the constraints of the study.

Product groups with the highest savings potential and/or for which an appropriate inclusion of resource efficiency aspects could be identified, will subsequently be subject to further revision studies to provide detailed technical and market data.

c) Conclusions of the report

The conclusion of this exploratory study is that for all product groups considered (with the exception of pumps and simple set top boxes) a revision of existing regulations (or introduction of new regulations) is the preferred policy option. The analysis shows that these product groups are expected to continue to meet eligibility criteria for the introduction of ecodesign and/or energy labelling measures, with simple set top boxes as sole exemption as its market and environmental significance is in rapid decline (sales are expected to be marginal by 2020).

The conclusions of the review study as regards lighting products are presented in a separate working paper.

The study identified the following product groups as "High or medium priority", requiring further (extensive/comprehensive) revision studies:

- Domestic cold appliances, as the energy saving potential is significant (at least 5 TWh/year in 2030), and an assessment of correction factors, number of product categories and the effect of a revised international test standard is required. In addition, there is a possibility for resource efficiency requirements. The revision should also include an assessment of possible ecodesign requirements for wine storage appliances.

- Domestic washing machines, despite their modest energy savings potential (3 TWh/year in 2030), as there is a possibility for resource efficiency requirements (in particular as regards water consumption and material efficiency), and a need to better understand the interaction between washing temperature, cycle duration, label information, actual load behaviour by users and appropriateness of introducing rinsing and spin drying requirements. The study should also include domestic washer-driers which should be aligned, or combined, with activities related to washing machines, as 'washing' appears to be a more prominent product function than 'drying'.

- Domestic dishwashers, despite the small energy savings potential (1.4 TWh/year in 2030), as there is a possibility for resource efficiency requirements (in particular as regards water consumption and material efficiency). Additionally, the introduction of a new test standard might incur changes on energy efficiency values, drying and cleaning performance and should be closely followed. A more extensive review should address issues for better alignment of the measurement and calculation method to real life use and the possibility for resource efficiency requirements.

The study also identified simple set top boxes as "low priority", requiring no further study. The significance of this product group will be reduced within the next decade and the energy savings potential is low (0.2-0.3 TWh/year in 2030). The resource efficiency related savings potential is estimated to be relatively significant compared to the direct energy but in absolute terms the impact is limited as sales will diminish drastically.

On water pumps, the exploratory study did not result in information that the existing regulation needs to be revised on the aspect of test tolerances, i.e. the allowed deviation between measured and declared values.

IV. Points for consultation

It is suggested to discuss the possibility to further revise product groups with the highest savings potential and/or for which an appropriate inclusion of resource efficiency aspects could be identified, i.e. domestic cold appliances, domestic washing machines (including washer dryers) and domestic dishwashers. These products will be subject to further revision studies to provide detailed technical and market data. The revision studies for these product groups will follow the MEErP methodology.

It is suggested to leave the current legislation in place for simple set top boxes and water pumps.