DRAFT

Commission communication in the framework of the implementation of Commission Regulation (EC) No 642/2009 of 22 July 2009 implementing Directive 2005/32/EC of the European Parliament and of the Council with regard to ecodesign requirements for televisions

(Text with EEA relevance)

Publication of titles and references of transitional methods of measurement for the implementation of Regulation (EC) No 642/2009 and, in particular, Annex II thereof.

| Measured parameter | Organisation | Reference | Title |
| --- | --- | --- | --- |
| On-mode power consumption – terms, definitions and abbreviations | IEC | Clause 3 of IEC 62087, Edition 2.0. Where Clause 3 of IEC 62087, Edition 2.0 conflicts with the definition set out in Article 2 of Regulation (EC) No 642, then that Regulation shall prevail. | Methods of measurement for the power consumption of audio, video and related equipment |
| On-mode power consumption – General method of measurement | IEC | Clause 5 of IEC 62087, Edition 2.0. Where Clause 5 of IEC 62087, Edition 2.0 conflicts with the Annex I, points 3 and 4, and with Annex II, point 1 of Regulation (EC) No 642, then that Regulation shall prevail. |  |
| On-mode power consumption – Measuring conditions for television sets in On (average) mode | IEC | Clause 11, points 1-4 and point 6 of IEC 62087, Edition 2.0. Where Clause 6 of IEC 62087, Edition 2.0 conflicts with the Annex I, points 3 and 4, and with Annex II, point 1 of Regulation (EC) No 642, then that Regulation shall prevail. |  |

| Standby/off-mode power consumption – terms and definitions | CENELEC | Clause 3 of EN 62301, First Edition. Where Clause 3 of EN 62301, First Edition conflicts with Article 2 of Regulation (EC) No 642, then that Regulation shall prevail. | Household electrical appliances – Measurement of standby power |
| --- | --- | --- | --- |
| Standby/off-mode power consumption – General conditions for measurements | CENELEC | Clause 4 of EN 62301, First Edition. Where Clause 4 of EN 62301, First Edition conflicts with Annex II, point 2 of Regulation (EC) No 642, then that Regulation shall prevail. |  |
| Standby/off-mode power consumption – Measurements | CENELEC | Clause 5 of EN 62301, First Edition. Where Clause 4 of EN 62301, First Edition conflicts with Annex II, point 2 of Regulation (EC) No 642, then that Regulation shall prevail. |  |

# Footnotes

It is intended that these transitional methods will ultimately be replaced by harmonised standard(s). When available, reference(s) to the harmonised standard(s) will be published in the Official Journal of the European Union in accordance with Articles 9 and 10 of Directive 2009/125/EC.